## Slide 1: Coexistence of Heterogeneous Traffic in CSMA/CA Networks
Tamir Husain
Christopher A. Wood

## Slide 2: Agenda
Problem statement
Markov model iterations
Simulation overview
Experimental results and observations
Q&A

## Slide 3: Traffic Trends
Application traffic is becoming increasingly heterogeneous:
  Real-time video streaming (e.g., Netflix)
  Web browsing
  File downloads
  VoIP (e.g., Skype)
  Video games
  …
Emerging traffic types vary in packet size, interarrival times, bursty-ness, etc.
Many applications send and receive traffic over wireless PHY mediums – WiFi

## Slide 4: 802.11 Distributed Control Function
A simplistic random access scheme based on the CSMA/CA protocol.
Failed packets are retried according to a binary exponential backoff rule.
  At each packet transmission, the backoff is uniformly in the range (0, w-1)
  The window w is set to Wmin to begin, and upon every failure, the backoff counter window is doubled.
  The maximum backoff time is bounded by Wmax = 2mWmin.
Selections of Wmin and Wmax depend on the physical layer specifications in the 802.11 standard

## Slide 5: The DCF Model with Saturated Traffic
Buffer

## Slide 6: Question 1
How does the performance of the DCF vary with increasingly heterogeneous traffic?

## Slide 7: Question 2
Is universal random backoff the best technique technique to handle collisions? Would a deterministic avoidance scheme be better suited for heterogeneous traffic? Or maybe a hybrid approach?

## Slide 8: Question 3
Should backoffs be tailored to the type of traffic?

## Slide 9: Research Approach
Create Markov models that represent varying types of traffic:
  Media streams
  Web browsing
  File downloads
Compute metrics for each of these models individually, i.e., with a constant conditional collision probability
Compute metrics when different Markov models of these types are superimposed
Analyze the data

## Slide 10: Supporting Unsaturated Traffic

## Slide 11: Creating a more complex DCF
Adding features adds new dimensions to the 2D DCF
  Packetsize, interarrival, postbackoff, etc…
Create small Markov models
  Treat each as a black box
  Connect them through instantaneous transitions
Compressible states
  Temporary logical states
  Probabilities distributed to real states in preprocessing

## Slide 12: Compressible States
x1
x2
a
b
c
s
0.5
0.25
0.25
0.8
0.2
1.0
Uncompressed Model
s, a, b, c: Traditional states
x1, x2: Compressible States
  “execution time” = 0

## Slide 13: Compressible States
x1
x2
a
b
c
s
0.5
0.25
0.25
0.8
0.2
1.0
a
b
c
s
0.25 + 0.25 * 1.0 = 0.5
0.5 * 0.8 = 0.4
0.5 * 0.2 = 0.1
Uncompressed Model
Compressed Model

## Slide 14: Compressible DCF
Blue: Original DCF Transmit
Yellow: Original DCF Backoff
Green: Compressible states
1,1
1,2
2,1
2,2
2,3
2,4
failure, 1
success
transmit
failure, 2

## Slide 15: Adding Interarrival
Blue: Original DCF Transmit
Yellow: Original DCF Backoff
Green: Compressible states
Orange: Interarrival
3
2
1
interarrival
1,1
1,2
2,1
2,2
2,3
2,4
failure, 1
success
transmit
failure, 2

## Slide 16: Adding Packetsize Chains (a new dimension)
success
3
2
1
interarrival
Blue: Original DCF Transmit
Yellow: Original DCF Backoff
Green: Compressible states
Orange: Interarrival
Red: Packet Size
packet size
calculation

## Slide 17: Variable Packet Size

## Slide 18: Varying Packet Types
Packet types differ in size and frequency of arrival
  I-Frame packets are larger but less frequent. B/P-Frame packets are more numerous but smaller
  Web traffic may download a small HTML file followed by many large images.
  Each packet type has a “fixed” packet size, decided at the beginning of the lifetime of the packet
    Fixed for the lifetime of the duration, but “calculated” through the markov model
Packet type transitions may be deterministic

## Slide 19: Traffic Models
We focus on three types of traffic
  Multimedia
  Web browsing
  File downloads
Each traffic can be characterized according to
  Packet size
  Interarrival time and packet queue saturation
  Type of packet
Consequence: our model needs to parameterize each of these characteristics to model each type of traffic

## Slide 20: Web Traffic
Primary characteristics
  Randomly sized packets
  Random interarrival time
Parameters to tune:
  Packet size (random)
  Interarrival time (random)
Tx
Wait
Size

## Slide 21: Web Traffic Illustrated
Size Chain
Success
Wait
Fail
time

## Slide 22: File Downloads
Primary characteristics:
  Long periods of activity and long inter-burst time
  Usually large packet sizes
Parameters to tune:
  Packet size (high)
  Queue arrival time (long)
  Interarrival time (short)
Tx
Wait
Size

## Slide 23: File Downloads Illustrated
Size Chain
Success
Wait
Fail
Interarrival
Collapsible
time

## Slide 24: Multimedia Traffic
Primary characteristics:
  Streams of different types of packets, each of a different length
Parameters to tune:
  Packet size
  Packet type
Tx
Wait
Size
Switch Type

## Slide 25: Multimedia Traffic
MPEG-4 packet types include I/B/P Frames
  GOP (group of pictures) ordering determines type
    I B B P B B P B B P…etc
  I-Frames are key frames, full images, no references
    1 I-Frame per GOP. Around 2/second
  P-Frames use data from previous frames
    Comes in repeated groups of BBP. Around 10/sec
  B-Frames are bi-directional. Heavily compressed
    Around 20/second

## Slide 26: Multimedia Illustrated
Size Chain
Success
Wait
Fail
Interarrival
Collapsible
time

## Slide 27: All Together
Web
Browsing
File
Downloads
Multimedia
Streaming
time

## Slide 28: Experimental Metrics
Average and individual node:
  Throughput (cumulative and variance)
  Idle time (backoff, post-backoff)
  Packet transmit probability
  Packet loss probability

## Slide 29: The Case for Small Backoffs
Simulations with large backoff values make metrics less “visible”

## Slide 30: The Case for Few Nodes
Simulations with many nodes obfuscate the effects of traffic parameters

## Slide 31: Experimental Setup
Choose one fixed random node
Choose another node of the target traffic type and vary a single parameters,
  Interarrival time (chain length)
  Packet size distribution
  Likelihood of entering an interarrival chain

## Slide 32: File Downloads: Varying Interarrival Time
Packet Size = [1]
Packet Size = [1,2,3,4,5]

## Slide 33: File Downloads: Varying Packet Size
Packet Size = [1]
Packet Size = [1,2,3,4,5]

## Slide 34: Observations
Average throughput increases as the time between file download bursts of packets increases
Average throughput increases as the size of packets increases
Download throughput is starved due to increasing packet sizes and long interarrival time (longer time between attempts)
Long times between bursts leave more room for other nodes to transmit

## Slide 35: Web Browsing: Probability Traffic Gaps
Packet Size = [1]
Packet Size = [1,2,3,4,5]

## Slide 36: Observations
For small gaps, random node throughput unaffected
For large gaps, random node throughput increases with respect
Overall: Sporadic nature of web traffic characteristics favors other nodes in the system

## Slide 37: Multimedia: Varying Streaming BPS
Packet Size = [1]
Packet Size = [1,2,3,4,5]

## Slide 38: Observations
Higher streaming constraints starve other nodes in the network
  Multimedia node throughput increases and random node throughput decreases as a function of streaming quality
Small packet sizes for random nodes aren’t affected by multimedia streaming
  Probable cause: streams of traffic are mixed together

## Slide 39: Conclusions
The 802.11 DCF function behaves differently depending on the type of traffic being transmitted
Throughput quickly degrades as more than one node is using the channel (higher collision probability)
Application-agnostic random backoffs are perhaps not the best choice for collision avoidance when dealing with non-multimedia streams
Random backoffs serve multimedia traffic quite well in the presence of other nodes

## Slide 40: Questions?