## Slide 1: Coexistence of Heterogeneous Traffic in CSMA/CA Networks
Tamir Husain
Christopher A. Wood

## Slide 2: Agenda
Problem statement
Markov model iterations
Simulation overview
Experimental results and observations
Q&A

## Slide 3: Traffic Trends
Application traffic is becoming increasingly heterogeneous:
  Real-time video streaming (e.g., Netflix)
  Web browsing
  File downloads
  VoIP (e.g., Skype)
New traffic types vary in packet size, interarrival times, burstyness, etc.
Most applications send and receive traffic over wireless PHY mediums – WiFi

## Slide 4: Problem Statement
Question 1: How does the performance of CSMA/CA vary with increasingly heterogeneous traffic?
Question 2: Is universal random backoff the best technique technique to handle collisions? Would a deterministic avoidance scheme be better suited for heterogeneous traffic? Or maybe a hybrid approach?
Question 3: Should backoffs be tailored to the type of traffic?

## Slide 5: Research Approach
Create Markov models that represent varying types of traffic:
  Media streams
  Web browsing
  File downloads
Compute metrics for each of these models individually, i.e., with a constant conditional collision probability
Compute metrics when different Markov models of these types are superimposed
Analyze the data

## Slide 6: 802.11 Distributed Control Function
A simplistic random access scheme based on the CSMA/CA protocol.
Failed packets are retried according to a binary exponential backoff rule.
  At each packet transmission, the backoff is uniformly in the range (0, w-1)
  The window w is set to Wmin to begin, and upon every failure, the backoff counter is doubled.
  The maximum backoff is bounded by Wmax = 2mWmin.
Selections of Wmin and Wmaxare dependent upon the physical layer specifications in the 802.11 standard

## Slide 7: Traffic Models
We focus on three types of traffic
  Multimedia
  Web browsing
  File downloads
Each traffic can be characterized according to
  Packet size
  Interarrival time and packet queue saturation
  Type of packet
Consequence: our model needs to parameterize each of these characteristics to model each type of traffic

## Slide 8: The DCF Model with Saturated Traffic

## Slide 9: Supporting Unsaturated Traffic

## Slide 10: Size Chain Blackbox
Equal probability of entering each chain
Exit transition probability is a function of the chain length
P(success) = (1 – p)^n
n

## Slide 11: Variable Packet Size

## Slide 12: Interarrival Time

## Slide 13: Varying Packet Types
Packet types differ in size and frequency of arrival
  E.g., video I packets are larger and less frequent than smaller D packets
Each packet type has a “fixed” packet size, decided at the beginning of the lifetime of the packet
Packet type transitions are deterministic

## Slide 14: Web Traffic
Primary characteristics
  Randomly sized packets
  Random interarrival time
Parameters to tune:
  Packet size (random)
  Interarrival time (random)

## Slide 15: Web Traffic Illustrated
Wait
Failure
Success

## Slide 16: File Downloads
Primary characteristics:
  Long periods of activity and long inter-burst time
  Usually large packet sizes
Parameters to tune:
  Packet size (high)
  Queue arrival time (long)
  Interarrival time (short)

## Slide 17: File Downloads Illustrated
Wait
Failure
Success

## Slide 18: Multimedia Traffic
Primary characteristics:
  Streams of different types of packets, each of a different length
    E.g., Big I frames (packets) and many small D packets
Parameters to tune:
  Packet size
  Packet type

## Slide 19: Multimedia Illustrated
Wait
Failure
Success
Iframe Success

## Slide 20: All Together
Web
Browsing
File
Downloads
Multimedia
Streaming
time

## Slide 21: Experimental Metrics
Average and individual node:
  Throughput (cumulative and variance)
  Idle time (backoff, post-backoff)
  Packet transmit probability
  Packet loss probability